SECTION 12 34 00

LAMINATE CLAD CASEWORK

# PART 1 – PRODUCTS

1.01	ACCEPTABLE MANUFACTURERS:

- Manufacturer:

  - TMI Systems Corporation.

    - Drawings and specifications are based on manufacturer’s literature from TMI SYSTEMS CORPORATION, 50 South Third Avenue West, Dickinson, North Dakota, 58601, Phone: 800-456-6716, fixed modular, flexible rail mounted, and mobile casework and accessories.

    - Other manufacturers shall comply with the minimum levels of material and detailing indicated on the drawings or as specified.

1.02	CABINET HARDWARE

  - Pulls:

- Select from the TMI Antimicrobial Pull Program or other manufacturer’s pre-approved equivalent program.

- Pull program offering must include minimum of 6 metal pull design and finish option combinations including:

  - Pulls finished with Agion® silver ion coating, meeting US-EPA antimicrobial regulatory approval.  Include: Contemporary, Square, and Wire options.

  - Pulls with copper alloy core, meeting US-EPA antimicrobial regulatory approval.  Include: Bow, Bar, and Wire options.

ANTIMICROBIAL PULLS: SELECT ONE

- Pull Selection: Contemporary Pull (5-1/2 inch width with 128mm hole spacing) finished with Agion® silver ion coating meeting US-EPA antimicrobial regulatory approval.

- Pull Selection: Square Pull (5-1/2 inch width with 128mm hole spacing) finished with Agion® silver ion coating meeting US-EPA antimicrobial regulatory approval.

- Pull Selection: Wire Pull (4 inch width with 96mm hole spacing) finished with Agion® silver ion coating meeting US-EPA antimicrobial regulatory approval.

- Pull Selection: Bow Pull (6 inch width with 128mm hole spacing) with CuVerro® copper alloy core meeting US-EPA antimicrobial regulatory approval.

- Pull Selection: Bar Pull (4-3/4 inch width with 96mm hole spacing) with CuVerro® copper alloy core meeting US-EPA antimicrobial regulatory approval.

- Pull Selection: Wire Pull (4-1/4 inch width with 96mm hole spacing) with CuVerro® copper alloy core meeting US-EPA antimicrobial regulatory approval.

- Pull designs shall comply with the Americans with Disability Act (ADA).

1.03 	COLOR SELECTION:

    - Hardware Color Selection:

- Pulls: Select from design specific finish options available in the TMI Antimicrobial Pull Program.